The process of measuring structure-borne vibration differs significantly from that of vibrations in air. The task is complicated by several factors, the most obvious of which is the difficulty of measuring variables at any location besides the boundary. This predicament is exactly inverted in air-borne sound, where the measurement can easily occur within the field of interest, and boundary measurements are relegated to specialized sensors. \cite[p.~3]{Cremer} Furthermore, the variables which can be readily measured in traditional structure-borne acoustics are kinematic variables: displacement and its derivatives. Pressure---the old standby of air-borne acousticians---must typically be derived from these variables. Referring back to section \ref{sec:npwaveq_nd}, we can see that the structure-borne equivalent of acoustical pressure, stress, must be calculated as a 2^{nd}-rank tensor, because of its directionality.

Furthermore, the excursions of the kinematic variables in a solid as a result of vibratory stress can be quite small. The exact relationship between these variables depends primarily on the material's elasticity constants, $c_{ijkl}$, which are sensitive to the directionality and polarization of the vibratory motion, relative to the particles in the solid. See section \ref{sec:npwaveq_nd} for an introductory look at these considerations.

For example, given equation \eqref{recrelation}, we can calculate the ratio of the inter-particulate equilibrium length to the length under unit normal stress of a piece of polycrystalline aluminum with a density of $2,695 \frac{\text{kg}}{\text{m^2}}. This value will be the amount of compression observed as the result of $1 \frac{\text{N}}{\text{m}^2}$. Substituting in the value of $c_{11} = 11.1$, with units of $10^{10} \frac{N}{\text{m}^2}$,\cite[p.~12]{Ballantine} we find the material will deviate on the order of $\frac{1}{11.1E10}$ from its original position. Given the boundary conditions for a free surface (see section \ref{sec:lossy}), we conclude that the stress compression wave traveling through this material will be zero at the surface and the kinematic waves will be at a maximum magnitude.

Another rule of thumb to derive the orders of magnitude entailed by structure-borne sound is the maximal strain a given material can withstand before fracture. In the orders of magnitude near this limit, the constitutive relation equation \eqref{recrelation} no longer holds, and becomes nonlinear. For most materials, the strains in the nonlinear region between fracture and Hookean linearity are on the order of $10^{-3}$ to $10^{-5}. \cite[p.~16]{Ballantine}

Given these considerations, the direct observation of vibration in a solid is generally restricted to those in the possession of a microscope. However, many individuals have devised methods for indirectly observing such phenomena. A famous example occurred in 1787, in Wittenberg, Germany, where a 31 year-old Ernst Chladni first published the results of an experiment which would captivate the imaginations of scientists and laypeople alike.\cite{Stockman} \cite{Ullmann} His experiment, which will be discussed in greater depth in section \ref{} of this document, consisted of sprinkling a fine powder over the surface of an object, and setting it into vibration using a violin bow. The particles collected along the nodal lines, where the incident kinematic waves were at a minimum amplitude. The dynamic shapes and synesthetic correspondence between sight and sound helped to canonize acoustics as a legitimate scientific discipline.

The techniques discussed in pages that follow will be assessed according to a number of attributes: cost, field-readiness, quality, generality, and impedance. In this context, \emph{cost} refers to economic cost---measured in dollars, not flops. \emph{Field-readiness} is actually a cluster of concerns including mechanical robustness, portability, and ease of calibration. These considerations may take on a variety of forms, depending on the technique: for example tube lasers are not very field-ready because of their high power drain. The term \emph{quality}refers to the information content of the measurements, meaning linearity (or linearizability), signal-to-noise ratio (SNR), gain-bandwidth-product (GBP), and sensitivity. \emph{Generality} means we ask ''what can it measure?'' For example, a technique which measures perturbations in the magnetic field would be difficult to apply to the general case. Finally, \emph{impedance} refers not to electrical impedance---as any modern sensor can be reliably impedance-matched with proper gain-staging---but rather mechanical impedance, as explored in section \ref{sec:impedance}. Sometimes, despite our best efforts, these considerations will become interdependent. This is the nature of considerations.

Sensors that Require Inertial Coupling

A large number of structural vibration measurement devices require the mechanical coupling of the sensor to the object of interest. Even fairly recent articles in structural vibration analysis cite methods that involve these devices. \cite{han} \cite{kerschen} Using sensors which mechanically couple to the vibrating body has many advantages: they often provide high quality measurements with a low cost, extremely field-ready apparatus. Furthermore, many of these devices are reversible, meaning they can also serve as actuators. \cite[p.~69]{Cremer} In some applications, these sensors can be extremely precise, and can hone in on specific mode families within the material. \cite[p.~36]{ballantine}

The drawbacks to using mechanically coupled sensors most frequently involve the acoustic impedance load concomitant with their operation. All sensors have mass, and this mass times the acceleration due to gravity will always result in a normal stress being added to the system, in the location of the sensor. Recall that the characteristic impedance of a material is given by the stress over the particle velocity in the medium, or $T/\dot{u}$. If the impedance of the sensor is high enough, the dynamic behavior of the object changes. This can be somewhat ameliorated by ensuring the sensors are extremely lightweight, or perhaps by the clever use of suspension springs. \cite[p.~4]{\Cremer} Recall from section \ref{sec:impedance} that at an interface between two impedances $Z_1$ and $Z_2$, if $Z_2$ is much higher than $Z_1$, the reflected wave will not be completely inverted at the interface, and a partial standing-wave will result. The least adversely affected frequencies are those for which the sensor has a resonance. Since the sensor's inertial and restorative forces are $\pi$ apart in phase at such frequencies, the impedance will tend toward zero. However, the severely limited bandwidth of such a measuring device would not make for a particularly good sensor. \cite[p.~9]{Cremer}

The carbon microphone is an element which changes its resistance in response to strain. The principle of operation is simple: carbon particles are suspended in a insulating substrate, which are pressed together when the material exhibits strain. A voltage across the element encodes the strain into changes in current. This type of instrument is very light-weight, cheap, and can be made into force sensing resistors (FSR's) and strain gauges. However, carbon microphones do not have reasonable signal to noise ratios or bandwidths for high-quality vibration sensing. Furthermore, they are fairly easily damaged. Their generality is also questionable, since they must be glued onto the object of study. They do, however, work fairly well for measuring low frequencies. \cite[p~.26]{Cremer}

Variable inductance sensors typically measure displacement. They are usually implemented with an alternating voltage, and the displacement is encoded into the current. This approach allows the engineer to filter out interference sidebands easily. However, the carrier frequency must high enough that the entire bandwidth of interest can pass through without artifacts. Typically the usable bandwidth is from DC to about one quarter the carrier frequency. This technique encodes the signal onto the amplitude of the carrier wave. An alternative to the variable inductance method is to use an LC oscillator with the inductor safely hidden within the housing, and instead measuring variable capacitance. In this case, the frequency of the circuit will vary as
\omega_0 = \frac{1}{\sqrt{LC}},

although there will also be some amplitude modulation as well. The second plate of the capacitor may either be the object itself or some foil attached to it. The variable capacitance sensor can measure very small excursions of the material. The mechanical impedance entailed by this method can be fairly low, at least in comparison to others in its family. However, the technique is susceptible to interference, and not particularly field-ready. \cite{Cremer}

By far, the most common type of coupled instrument for structure-borne sound is the piezoelectric transducer (PZT). These devices are extremely convenient and cheap. Furthermore, they can be made to be quite accurate. Because of the potentially high efficiency with which these devices can convert energy from stress to current and back, PZT's are desirable in low power or high frequency applications. When used as sensors, they can be made to approach ideal accelerometers. \cite[p.~67]{Cremer}

Piezoelectric materials are generally crystals or, less often, amorphous ceramics that have asymmetries in their atomic lattice. \cite[p.~17]{Kino} These materials have a different set of constitutive relations, and therefore a different wave equation, which explains the lengthy title of section \ref{sec:npwaveq_nd}. These materials exhibit coupling between strain and electrical polarization, which is the result of unevenly distributed charges in the lattice. This coupling results in two effects, which are always observed together: the \emph{direct} piezoelectric effect, wherein the material develops a macroscopic net charge distribution as the result of mechanical strain, and the \emph{converse} piezoelectric effect, wherein mechanical strain occurs as the result of the application of an electric field. \cite[p.~23]{Ballantine} The constitutive relations for piezoelectric materials may be derived from an adjustment of the non-piezoelectric elastic constitutive relations, as defined in equation \eqref{ecrelations}, by adding a second equation, resulting in a system of equations\cite[p.~24]{Ballantine},

T_I = \sum_{J=1}^6 \left( c_{IJ}^ES_J - \sum_{j=1}^3 e_{Ij}E_j \right) \notag\\
D_i = \sum_{j = 1}^3 \left( \epsilon_{ij}^S E_j + \sum_{J = 1}^6 e_iJ S_J \right) \qquad \text{,}

A large number of structural vibration measurement devices require the mechanical coupling of the sensor to the object of interest. Even fairly recent articles in structural vibration analysis cite methods that involve these devices. \cite{Han2003} \cite{Kerschen2002} Using sensors which mechanically couple to the vibrating body has many advantages: they often provide high quality measurements with a low cost, extremely field-ready apparatus. Furthermore, many of these devices are reversible, meaning they can also serve as actuators. \cite[p.~69]{Cremer1973} In some applications, these sensors can be extremely precise, and can hone in on specific mode families within the material. \cite[p.~36]{Ballantine1997}

The drawbacks to using mechanically coupled sensors most frequently involve the acoustic impedance load concomitant with their operation. All sensors have mass, and this mass times the acceleration due to gravity will always result in a normal stress being added to the system, in the location of the sensor. Recall that the characteristic impedance of a material is given by the stress over the particle velocity in the medium, or $T/\dot{u}$. If the impedance of the sensor is high enough, the dynamic behavior of the object changes. This can be somewhat ameliorated by ensuring the sensors are extremely lightweight, or perhaps by the clever use of suspension springs. \cite[p.~4]{Cremer1973} Recall from section \ref{sec:impedance} that at an interface between two impedances $Z_1$ and $Z_2$, if $Z_2$ is much higher than $Z_1$, the reflected wave will not be completely inverted at the interface, and a partial standing-wave will result. The least adversely affected frequencies are those for which the sensor has a resonance. Since the sensor's inertial and restorative forces are $\pi$ apart in phase at such frequencies, the impedance will tend toward zero. However, the severely limited bandwidth of such a measuring device would not make for a particularly good sensor. \cite[p.~9]{Cremer1973}

The carbon microphone is an element which changes its resistance in response to strain. The principle of operation is simple: carbon particles are suspended in a insulating substrate, which are pressed together when the material exhibits strain. A voltage across the element encodes the strain into changes in current. This type of instrument is very light-weight, cheap, and can be made into force sensing resistors (FSR's) and strain gauges. However, carbon microphones do not have reasonable signal to noise ratios or bandwidths for high-quality vibration sensing. Furthermore, they are fairly easily damaged. Their generality is also questionable, since they must be glued onto the object of study. They do, however, work fairly well for measuring low frequencies. \cite[p~.26]{Cremer1973}

Variable inductance sensors typically measure displacement. They are usually implemented with an alternating voltage, and the displacement is encoded into the current. This approach allows the engineer to filter out interference sidebands easily. However, the carrier frequency must high enough that the entire bandwidth of interest can pass through without artifacts. Typically the usable bandwidth is from DC to about one quarter the carrier frequency. This technique encodes the signal onto the amplitude of the carrier wave. An alternative to the variable inductance method is to use an LC oscillator with the inductor safely hidden within the housing, and instead measuring variable capacitance. In this case, the frequency of the circuit will vary as
\begin{equation*}
\omega_0 = \frac{1}{\sqrt{LC}} \text{,}
\end{equation*}
although there will also be some amplitude modulation as well. The second plate of the capacitor may either be the object itself or some foil attached to it. The variable capacitance sensor can measure very small excursions of the material. The mechanical impedance entailed by this method can be fairly low, at least in comparison to others in its family. However, the technique is susceptible to interference, and not particularly field-ready. \cite{Cremer1973}

By far, the most common type of coupled instrument for structure-borne sound is the piezoelectric transducer (PZT). These devices are extremely convenient and cheap. Furthermore, they can be made to be quite accurate. Because of the potentially high efficiency with which these devices can convert energy from stress to current and back, PZT's are desirable in low power or high frequency applications. When used as sensors, they can be made to approach ideal accelerometers. \cite[p.~67]{Cremer1973}

Piezoelectric materials are generally crystals or, less often, amorphous ceramics that have asymmetries in their atomic lattice. \cite[p.~17]{Kino1987} These materials have a different set of constitutive relations, and therefore a different wave equation, which explains the lengthy title of section \ref{sec:npwaveq_nd}. These materials exhibit coupling between strain and electrical polarization, which is the result of unevenly distributed charges in the lattice. This coupling results in two effects, which are always observed together: the \emph{direct} piezoelectric effect, wherein the material develops a macroscopic net charge distribution as the result of mechanical strain, and the \emph{converse} piezoelectric effect, wherein mechanical strain occurs as the result of the application of an electric field. \cite[p.~23]{Ballantine1997} The constitutive relations for piezoelectric materials may be derived from an adjustment of the non-piezoelectric elastic constitutive relations, as defined in equation \eqref{ecrelation}, by adding a second equation, resulting in a system of equations\cite[p.~24]{Ballantine1997},
\begin{align}\label{pecrelation}
T_I &= \sum_{J=1}^6 \left( c_{IJ}^E S_J - \sum_{j=1}^3 e_{Ij}E_j \right) \notag\\
D_i &= \sum_{j = 1}^3 \left( \epsilon_{ij}^S E_j + \sum_{J = 1}^6 e_{iJ} S_J \right) \qquad \text{,}
\end{align}

where $e_{Ij}$ is a 3\textsuperscript{rd}-rank tensor in reduced notation (see section \ref{sec:npwaveq_nd}) describing the piezoelectric stress constants, D_i is a 1\textsuperscript{st}-rank tensor containing the electrical displacement components, $\epsilon_{ij}$ is a 2\textsuperscript{nd}-rank tensor of the permittivity constants, and $E_j$ is a 1\textsuperscript{st}-rank tensor containing the electric field components. \cite[p.~24]{Ballantine}$c_{IJ}^E$ is analogous to the elasticity tensor, $c_{IJ}$, from equation \eqref{recrelation}, except that we have now defined its components for the condition of zero electric field. \cite[p.~19]{Kino} The above system of equations shows the nature of the interdependence of the electric and mechanical variables: stress relates to strain through the elasticity constants $c$ (as usual), and to the electric field through the piezoelectric stress constants $e$, while the electric displacement $D$ relates to the electric field $E$ through the permittivity constants $\epsilon$, and to the strain through the piezoelectric stress constants once again. The entire system forms a loop of dependence among the variables. A piezoelectric solid requires $3\times6 = 18$ constants to describe each of these relationships, and thus fully characterize it. Furthermore, strain patterns will vary with the piezoelectric material chosen. \cite[p.~24]{Ballantine}

From the constitutive relations defined in equations \eqref{pecrelation}, we can now derive the \emph{Piezoelectric Wave Equation} in a few simple steps. First, we note that the electric field components, $E$, can be written in terms of potential, $\phi$, as $E_k = {}^{-\partial \phi}/_{\partial x_k}$. We also note that $S_J = {}^{\partial u_l}/_{\partial x_k}$, which comes from \eqref{recrelation}. Substituting these into our definition of $T_I$ from \eqref{pecrelation}, we find\cite[p.~26]{Ballantine}

T_{ij} = \sum_{J=1}^6 \left( c_{IJ}^E \frac{\partial u_l}{\partial x_k}\right) + \sum_{k=1}^3 \left( e_{Ik} \frac{\partial \phi}{\partial x_k} \right) \qquad \text{,}

differentiating both sides with respect to $x_j$, and noting, just as we did in \eqref{motion}, that ${}^{\partial T_I} /_\partial x_j = \rho \ddot{u_i}$ gives the piezoelectric wave equation:

\rho\ddot{u_i} = \sum_{j,k,l = 1}^3 \left( c_{ijkl} \frac{\partial^2 u_l}{\partial x_k \partial x_j} \right)
+ \sum_{j,k=1}^3 e_{ijk}\left( \frac{\partial^2 \phi}{\partial x_k \partial x_j} \right)

//-uncopied

The above system represents 3 equations, but there are four unknowns: $u_{xyz}$ and $\phi$. If we believe the divergence of electric displacement $\nabla \cdot D = 0$, which is true for a piezoelectric solid with no free charges, we can find the fourth equation to be\cite[p.~27]{Ballantine}
\begin{equation}\label{pwaveq_phi}
\sum_{i,k,l=1}^3 e_{ikl}\frac{\partial^2 u_l}{\partial x_k \partial_i} - \sum_{i,k=1}^3 \epsilon_{ik} \frac{\partial^2 \phi}{\partial x_k \partial x_i} = 0 \qquad \text{.}
\end{equation}

Piezoelectric coupling changes the effective elasticity coefficient $c$. To find this effect, we solve the system of equations for a plane shear wave. We start by setting two of our particle displacement components, $u$, to zero, and combining equations \eqref{pwaveq} and \eqref{pwaveq_phi}. Since our hypothetical wave only has displacement coefficients along a single component---notated as $x_i$---we will drop the tensor notation for clarity. \cite[p.~27]{Ballantine}
\begin{align}
c \frac{\partial^2 u}{\partial x_i^2} + e \frac{\partial^2 \phi}{\partial x^2} = \rho \ddot{u}\label{pwaveq_plane}\\
e \frac{\partial^2 u}{\partial x_i^2} - \epsilon \frac{\partial^2 \phi}{\partial x^2} = 0\notag
\end{align}
Manipulating the the second equation's $\phi$ term to enable subtracting it from the first equation yields:
\begin{equation*}
\frac{e^2}{\epsilon} \frac{\partial^2 u}{\partial x^2} - e \frac{\partial^2 \phi}{\partial x^2} = 0 \qquad \text{,}
\end{equation*}
which can now be subtracted from \eqref{pwaveq_plane},
\begin{equation*}
\left(\frac{e^2}{\epsilon} + c\right) \frac{\partial^2u}{\partial x^2} = \rho \ddot{u} \qquad \text{.}
\end{equation*}
Comparing the left-hand side of the above equation to that of equation \eqref{npwaveq_nd} shows the relationship between the elasticity coefficient $c'$ in a material exhibiting piezoelectric coupling, and the elasticity coefficient $c$ in a material not exhibiting such coupling (for that vibratory regime), all other things being equal, to be
\begin{align*}
c' = c\left( 1 + \frac{e^2}{c \epsilon}\right)
c' = c (1 + K^2) \qquad \text{.}
\end{align*}
This value, $K^2 = {}^{e^2}/{}_{c \epsilon}$, is called the \emph{electromechanical coupling coefficient}, and it is given for a wave with a specific propagation direction and specific particulate displacement direction, on a particular material. Thus, it has the same dimensionality as $c$. \cite[p.~28]{Ballantine}

//---

As electromechanical resonators, PZT's have high selectivity, which allows them to be used as efficient oscillators and filters. \cite[p.~27]{Kino} There are several variants of PZT's, each one sensing a different mode of vibration. However, the vibrations most of these devices are intended to sense are forced. \cite[p.~154]{Cremer} Therefore, despite their novelty, their applicability to the topic at hand---that of spatially measuring acoustic vibration in the field---is fatally limited. The most applicable to vibration measurement appears to be the Thickness Shear Mode resonator.

\emph{Thickness Shear Mode resonators} (TSM), as their name implies, act on the shear mode of vibration as it propagates the thickness of the crystal. These are the kind of sensors typically used as ``contact microphones,'' which amplify strain waves directly into fluctuating voltages. However, TSM resonators are much more sensitive when driven to resonance. By tracking fluctuations in the resonant frequency of the crystal, a rigidly bound mass may be measured. \cite[p.~37]{Ballantine}

The measurement works using the fairly simple hypothesis offered by Lord Rayleigh: that the mechanical resonance only occurs when the peak kinetic energy balances the peak potential energy in a system. A mass that has been rigidly coupled to the surface of the crystal results in a change in kinetic energy, since the surface is naturally an anti-node for the strain wave, without a change in potential energy, which is zero at the surface regardless. \cite[p.~43]{Ballantine}

Recall from earlier discussions of the boundary behaviors of a vibrating body \ref{sec:impedance} that the incident surface of a reflected wave is the result of a change in impedance. When the impedance of at the surface is zero, the reflection is $\pi$, and the shear wave traveling across the sensor matches the resonance given by the object alone. However, if the impedance on the other side of the interface is nonzero, the wave is no longer rotated by $\pi$, and in the case of our forced vibration in section \ref{sec:impedance}, a partial standing wave resulted. \cite[p.~119]{Cremer} In this case, the vibration is not held at a given frequency, but rather held at resonance, so the frequency of the vibration changes to match the impedance ratio at the barrier.

The quality of TSM measurements, when applied correctly, is outstanding: the sensor can be driven at any of the thickness shear modes, which, similarly to the example we gave in section \ref{sec:modes}, would favor odd integer multiples of the zero-th modal wave-number, itself likely in the megahertz range. The sensitivity of the TSM is given by the \emph{Sauerbrey equation},
\begin{equation*}
\delta f = - \frac{2 f_1^2 \rho_s}{sqrt{\mu_q \rho_q}} \qquad \text{,}
\end{equation*}
where $\rho_s$ is the surface mass density, or mass per unit area. Since the fluctuations of frequency as the result of incident mass density are proportional to the square of the resonant frequency, this technique can be calibrated to many applications, particularly in the medical and chemical fields.

Although they vary over a wide range, the transducer itself is fairly cheap, and the implementation circuit is fairly simple. The frequency and stability of the crystal are the two primary factors in the cost vs quality curve. Digitizing the signal with consumer audio equipment would require heterodyning with a high frequency oscillator, perhaps also supplied by a crystal for stability purposes.

The measurement is only precise when the object of interest is thin in comparison with the wavelength of the vibration. This is because a reflection from the opposite boundary of the object measured would then cause its own reflections, and in fact would behave similarly to the coupled sensor as described earlier in this section. As a result of this, typically TSM's are used to measure the mass of rigid, thin films. Therefore, generality is not a strong point of this technique.

We previously discussed \emph{Surface Acoustic Waves} in section \ref{sec:waves}, in the context of boundary interactions in vibrating objects. These waves have practical uses mostly related to communications and non-destructive testing. That being said, the field of SAW devices is ripe for development. The basic idea for a SAW device is to line a material with strips of piezoelectric material, which alternate to form a pattern that corresponds to the mode of vibration of interest. These striated PZT's, called \emph{Interdigital Transducers}, can be either sensors or transducers. Frequently, these are designed as two-port devices. \cite[p.~36]{Ballantine}

Exciting work has been done using ultrasound to create acoustic holograms, and some results seem to be of promising quality. The prospect of imaging with sound is especially interesting when one considers the possibility of directly measuring longitudinal waves in solids, for example. However these devices fail on almost all fronts: they are still extremely expensive, laboratory-dwelling, application-specific devices. \cite[p.~276]{Kino} PZT's, we will soon discover, have more useful applications because of their interactions with light.

Piezoelectrics, again, for our purposes, seem to have more useful applications because of their ability to interact with light. Exciting work has been done using ultrasound to create acoustic holograms, and some results seem to be of promising quality. The prospect of imaging with sound is especially interesting when one considers the possibility of directly measuring longitudinal waves in solids, for example.

Many meaningful parallels may be drawn between optics and acoustics. The differential wave equation is the same, and the boundary conditions are very similar. Much like in acoustics, optics talks about wave-trains and beams, and, much like in acoustics, these are just conveniences: light doesn't travel in rays, any more than sound does. \cite[p.~100]{Hecht} Both are particles... occasionally.

//-----

Considerations for Optical Techniques
III)	Description and Assessment of Vibrometry Techniques that Do Not Require Coupling
A)	Considerations for Optical Techniques
1)	Characterization of Gaussian Laser Ray Bundles

The characterization of light sources is essential for any optical imaging application. Like sound, light can be described as a wave phenomenon: a solution to the differential wave equation. This time, the from the differential form of Maxwell's equations for free space. This model is known as the \emph{Classical} model, and we will largely content ourselves with this oversimplification, just as we did for acoustics earlier in this document. The vector formulation of Maxwell's equations is concisely descriptive: \cite[p.~44]{Hecht}
\begin{align}\label{maxwell}
\nabla^2 E &= \epsilon_0 \mu_0 \frac{\partial^2 E}{\partial t^2} \notag\\
\nabla^2 B &= \epsilon_0 \mu_0 \frac{\partial^2 B}{\partial t^2}
\end{align}
Above, $E$ and $B$ are vectors with $x, y,$ and $z$ components. $\epsilon_0$ and $\mu_0$ are the permittivity and permeability of free space, respectively. Thus, the propagation speed of such a disturbance (in a vacuum) is $v = 1/\sqrt{\epsilon_0 \mu_0}$. Light is a coupled electromagnetic field disturbance---that is, an electric and magnetic field, moving in synchrony---each component of which satisfies the scalar differential wave equation, just as we saw for sound in section \ref{sec:npwaveq}. That equation, which we have seen before in terms of exponential functions in equation \eqref{npwaveq}, looks like this when written more generally. \cite[p.~44]{Hecht}
\begin{equation}\label{waveq_light}
\frac{\partial^2\Psi}{\partial x^2} + \frac{\partial^2 \Psi}{\partial y^2} + \frac{\partial^2 \Psi}{\partial^2\Psi}{\partial z^2}= \frac{1}{v_0^2}\frac{\partial^2\Psi}{\partial t^2}
\end{equation}
We will once again restrict our discussion of wave propagation to harmonic plane waves, without loss of generality (vis. section \ref{sec:lossy}) because light behaves linearly at relatively small amplitudes, just like sound.\cite[p.~286]{Hecht} Recall that harmonic waves are of the form, e.g., $e^{-\mathsf{i}(\omega t \pm kx)}$. Harmonic waves are also called \emph{monochromatic}, in the context of light. In a vacuum, both constituent fields of light propagate in transverse waves, and they are in phase. Their axes of displacement are not only perpendicular to their propagation direction, but to each other. Plane waves can therefore be oriented, or \emph{polarized}, by rotating these vectors along the plane of constant phase.\cite[p.~45]{Hecht}

Just like acoustic waves, electromagnetic waves transmit energy without globally translating matter, according to the classical model. We can now define the energy per unit volume of a traveling harmonic plane wave. This invites cautious analogies to equation \eqref{kinetic}:
\begin{align}\label{em_energy}
W_E = \frac{\epsilon_0 E^2}{2}\notag\\
W_B = \frac{\mu_0 B^2}{2}\qquad \text{,}
\end{align}
with the notable difference that with light, we have two field variables to keep track of, whereas acoustic waves only had kinetic energy. N.B. the above equations are distinct from our treatment in section \ref{sec:lossy} of kinetic versus potential energy. While in acoustics, we described impedance and damping in terms of complex numbers, which changed the phase relationships between $W_k$ and $W_p$, this is not the case with $W_E$ and $W_B$. The electric and magnetic fields cannot be out of phase with one another: doing so would violate Maxwell's Equations. \cite[p.~46]{Hecht} Because these two disturbances are always connected to each other---with a real-valued constant, no less---the description of one field disturbance or another is typically sufficient. The standard conceit is to describe the $E$-field, since its magnitudes are much ``larger.'' A simple manipulation of Maxwell's Equations reveals by how much (for plane waves): \cite[p.~45]{Hecht}
\begin{equation}\label{EvB}
E_i = v_0 B_j \qquad \text{,}
\end{equation}
where $v_0$ is $2.997E8$ meters per second. The \emph{energy} in each field, however, is the same. The total energy per unit volume of the wave is then given by \cite[p.~46]{Hecht}
\begin{equation}\label{emEtotal}
$W_t = W_E + W_B = \epsilon_0 E^2 = \frac{B^2}{2} \qquad \text{.}
\end{equation}
To calculate the total power flow per unit area, we use the \emph{Poynting vector},
\begin{equation}\label{poynting}
S(x,y,z) = v_0^2 \epsilon_0 E(x,y,z) \times B(x,y,z)
\end{equation}
where the operator $\times$ denotes a cross-product. \cite[p.~46]{Hecht} The Poynting vector is an instantaneous measure that fluctuates in length with twice the frequency of the radiation. This makes it impossible to observe directly, and essentially meaningless for time-averaged values. Generally, to quantify the degree to which something is illuminated, the measure to use is \emph{irradiance}. Irradiance is the field variable that most sensors will measure. It is defined by
\begin{align}\label{irradiance}
I = \epsilon_0 v_0 \langle E^2 \rangle_T \qquad \text{,}
\end{align}
wherein the braces and the subscript, $\langle \rangle_T$, denote a time-average. \cite[p.~48]{Hecht}

The angle of reflection $\theta_r$, exhibited by a wavefront of light after striking a reflective surface, will always be equal to the angle of the wavefront's incident, $\theta_i$. When light travels through an appropriately transparent, non-dispersive material, the permittivity $\epsilon$ and permeability $\mu$, and, as a result, the velocity $v$, change. While this change in propagation velocity does not affect the temporal frequency (color) of the light, it alters the angle of transmitted light, $\theta_t$, and the amplitude of the reflected and transmitted components. The ratio which describes this change in propagation is called the \emph{relative index-of-refraction} between the two media and it is given by \emph{Snell's Law}\cite[p.97]{Hecht}:
\begin{equation}\label{snell_em}
\eta_ti \equiv \frac{\sin{\theta_i}}{\sin{theta_t}} = \frac{v_i}{v_t}
\end{equation}
In contrast to this value, which compares two materials, there is also an index-of-refraction $\eta$, which describes a given material's properties in relation to a vacuum. The incident, transmitted, and reflected vectors are all coplanar, and that plane is called the plane-of-incidence. To find the amplitudes and polarizations of the resulting refracted and reflected light, we must split the incident $E$-field into components which are parallel and perpendicular to this plane. Assuming the change in permeability is negligible, we can use the \emph{Fresnel equations}: \cite[p.~109]{Hecht}
\begin{align}\label{fresnel}
r_\perp \equiv \left( \frac{E_0r}{E_0i} \right)_\perp = \frac{n_i \cos{\theta_i} - n_t \cos{\theta_t}}{n_i \cos{\theta_i} + n_t \cos{\theta_t}}\notag\\
t_\perp \equiv \left( \frac{E_0t}{E_0i} \right)_\perp = \frac{2n_i \cos{\theta_i}}{n_i \cos{\theta_i} + n_t \cos{\theta_t}}\notag\\
r_\parallel \equiv \left( \frac{E_0r}{E_0i} \right)_\parallel = \frac{n_t \cos{\theta_i} - n_i \cos{\theta_t}}{n_i \cos{\theta_t} + n_t \cos{\theta_i}}\\
t_\parallel \equiv \left( \frac{E_0t}{E_0i} \right)_\parallel = \frac{2n_i \cos{\theta_i}}{n_i \cos{\theta_t} + n_t \cos{\theta_i}}\notag\\
\end{align}
These equations may be verified using the boundary conditions and Maxwell's equations. The boundary conditions require that the $E$-field component tangent to the boundary be continuous, while the $E$-field component normal to the boundary must rotate by $\pi$. N.B. for a given interface and polarization, may be an angle where $\theta_t = \pi / 2$, called the \emph{critical angle}. At this angle, all of the light is internally reflected. \cite[p.~112]{Hecht} Electromagnetic waves that propagate in this regime bear certain similarities to mechanical waves in SAW devices, in that their propagation is restricted. However, the similarities have more to do with the applications than with the physical phenomena. \cite[p.~440]{Kino}

It is common to simplify the propagation of waves into \emph{rays}: straight lines perpendicular to the wavefronts. The ray model loses a lot of detail, even in its description of free-space propagation, however it is beneficial for back-of-the-envelope estimates of some interactions. \cite[p.~95]{Hecht} Making the further assumption that such rays travel together in bundles which subtend only small angles from the main axis of an optical system, is called the \emph{Paraxial approximation}. This allows us to assume that optical components behave linearly, and as a result, many free-space optical systems can be easily modeled as matrix multiplications. \cite[p.~444]{Goodman} This technique, of constructing \emph{ray transfer matrices}, has implications for both modeling and regression analysis.

On the other hand, this assumes that all light travels as a plane wave, which is a fine assumption to make, until these waves start interfering with each other. \emph{Huygen's principle} is another useful approximation that suggests all the points of a propagating wavefront are the sources of spherical wavelets, which add together to form the wavefront at some later time. This assumption will help us visualize phenomena related to \emph{diffraction}. \cite[p.~100]{Hecht}

Diffraction is a broadly defined family of effects caused by the confinement of waves. It is caused by the constructive and destructive interference patterns endemic to all waves, exacerbated by the discontinuities in propagation factors at the boundaries. It is especially apparent when the extent of the wave's confinement is comparable to their wavelength. \cite[p.~32]{Goodman} However, diffraction is present in even the most finely calibrated optical systems.

Optical systems that are theoretically perfect---from a geometrical optics perspective, at least---are said to be ``diffraction limited.'' \cite[p.~143]{Hecht} There are several methods for describing the performance of the optical system in this state. These depend on application-specific assumptions, such as the coherence---chromatic purity, measured in average spatial beat length. Despite their differences, however, all of these measures somehow involve the \emph{Airy pattern}, a radially symmetric function of irradiance over deviation angle. The Airy pattern is essentially a cross-section of an ideal point-source at infinity, which has passed through an aperture at some point in the optical path, i.e., \cite[p.~445]{Hecht}
\begin{equation}\label{airy_patt}
I(\theta) = \left[ \frac{2 J_1 (ka \sin{\theta})}{ka \sin{\theta}} \right]^2 \qquad \text{,}
\end{equation}
where $J_1(u)$ is a Bessel function of the 1\textsuperscript{st} kind, order zero, $k$ is the spatial frequency of the light source, $a$ is the aperture radius, and $\theta$ is the angle of deviation from the center. \cite[p.~445]{Hecht}

By ``at infinity,'' we mean that the wavefronts of the point source---ostensibly spherical---have traveled sufficiently far to become plane waves. Since all lenses, mirrors, etc are of finite radius, we can assume any distant object fits this description. In the neighborhood of $\theta = 0$, this function is at a maximum. This circular region is known as the \emph{Airy disk}: \cite[p.~445]{Hecht}
\begin{equation}\label{\resolution}
\left( \delta \varphi \right)_{min} = \delta \theta = \frac{1.22 \lamdba}{D} \qquad \text{,}
\end{equation}
where $D$ is the diameter of the aperture, and $\lambda$ is the wavelength. This disk is the result of \emph{Fraunhofer} (far-field) diffraction, and the Airy pattern from equation \eqref{airy_patt} is the Fourier Transform of the aperture. \cite[p.~496]{Hecht} Sadly, time and space constraints preclude the author from providing this fascinating proof. However, an excellent form of it can be found in \cite[p.~104]{Goodman}.
2)	Development of M2 Classification of Laser Beam Quality

In order to reliably image vibration with laser light, we must characterize the beam. This will not only provide us with the means to interpret the results of imaging, but also provides us with a vocabulary to differentiate the quality of illumination sources. The most widely circulated model is currently the \emph{M^2} model, which includes a description of the ideal beam, and several distance measures which can characterize many aberrations. \cite[p.~4]{Marshall2004}

\emph{Lasers} use resonance to produce a beam of polarized, monochromatic light. In gas lasers, the resonance is produced in a halogen tube which is excited electrically. The excitation (or rather, the relaxation) process releases photons, which are initially scattered in all directions. Either end of the tube is affixed with high reflectance mirrors, one or both of which can also transmit light. Prior to reaching the mirrors, the light passes through angled polarizing filters, which only permit the emission of light whose $E$-field is parallel to the plane-of-incidence. \cite[p.564]{Hecht}

Light in this tube behaves like vibration in a solid object with two free ends. For reference, the case of a solid object with a single free end was discussed in section \ref{sec:modes}. The minimum round-trip length, which the light must traverse before emission is $2L$, if $L$ is the length of the tube. Light at this frequency would constitute the first longitudinal cavity mode. Note that these are not longitudinal waves. A given tube theoretically has an infinite number of these modes, at integer multiples of the fundamental. \cite[p.558]{Hecht}

In addition to longitudinal modes, the light inside the tube can exhibit standing waves that are transverse to the tube's axis as well. These modes are called \emph{Transverse Electric and Magnetic} modes, or $TEM_{mn}$ for short. $TEM_{mn}$ indeces refer to the mode number for each axis of symmetry, and prescribe much of the beam's behavior on exiting the tube. Depending on the construction of the laser, these irradiance profiles can be either rectangularly symmetric (Hermite-Gaussian),
\begin{equation}\label{rect_mode}
U_{mn}(x, y, z) = H_m(\frac{x}{w})H_n(\frac{y}{w})u(x,y,z)\qquad \text{,}
\end{equation}
where $H$ refers to a pair of Hermite polynomials, and $w$ is the radius of the beam, or circularly symmetric (Laguerre-Gaussian),
\begin{equation}\label{circ_mode}
U_{pl}(r, \varphi, z) = L_{pl}(\frac{r}{w}, \varphi)u(r, z)\qquad \text{,}
\end{equation}
where $L$ refers to a Laguerre polynomial, $r$ is a radial coordinate and $\varphi$ is an angular coordinate. \cite[p.~4]{Marshall} The function $u$ refers to the Gaussian Distribution, of the form
\begin{equation}\label{gauss}
u = \sqrt{ \frac{2}{\pi}} e^{-\frac{x^2 + y^2}{w^2}} = \sqrt{ \frac{2}{\pi}}e^{-\frac{r^2}{w^2}} \qquad \text{,}
\end{equation}
depending on the axis of symmetry. \cite[p.~5]{Marshall} In addition to these modes, there also exist \emph{degenerate modes}, notated as $TEM_{mn}^*$, which consist of two modes that share a frequency, arranged in quadrature. \cite[p.~6]{Marshall} These modes are loosely analogous to those found in plates.

Typical lasers exhibit several of these modes simultaneously. This is possible because modes are energetically orthogonal (cf. \ref{sec:modes}). However, the irradiance profile which best minimizes divergence from the collinear regime---due to diffraction---is the gaussian distribution, equation \eqref{\gauss}. \cite[p.~13]{Marshall} In mixed-mode beams, which are generally more tolerant to microscopic impurities on the lenses or mirrors, these spatial distortions, which amount to a hyperbolic change in width over the propagation length, grow more pronounced, and the length of the most focused range of the beam becomes much shorter. \cite[p.~14]{Marshall}Thus, the $M^2$ model compares the proportionality of a given beam, which might exhibit aberrations, to that of an ideal first mode gaussian. \cite[p.~15]{Marshall}

3)	Description of Transverse Electromagnetic Modes (TEM)
B)	Assessment of a Few Optical Vibrometry Techniques
1)	Backscatter Triangulation
2)	Structured Light (DLP) Methods
a)	Moire
b)	Digital Fringe Projection
3)	Interferometry
a)	michaelson interferometer
b)	Doppler vibrometer w/ phase unwrapping Bragg cell
c)	holographic vibrometry
c)	speckle interferometer
4)	Time-of-Flight Photography